## Slide 1: Edge detection

## Slide 2: Table of content
Intro to edges
Basic edge image
Edge thinning
  LoG
  NMS
Edge mask
Canny edge detector
Other edge related topics
  Frequency representation
  Unsharp filter

## Slide 3: Some motivation
Art
(Instagram filters)
Medicine
(tumor detection)
Robotics
(scene understanding)
Autonomous vehicles
(license plate detection)

## Slide 4: Why edges?
Representation of objects can be done without full image representation- more compact.
Edges are salient features (salient- “most noticeable or important”).

## Slide 5: What are edges?
“The outside limit of an object, area, or surface; a place or part farthest away from the center of something.”
Edges can be caused from many reasons in images:
depth discontinuity
surface color discontinuity
illumination discontinuity
surface normal discontinuity

## Slide 6: Representation in images
Rapid changes in colors.
Looks like steep edges if represented as a surface:

## Slide 7: Table of content
Intro to edges
Basic edge image
Edge thinning
  LoG
  NMS
Edge mask
Canny edge detector
Other edge related topics
  Frequency representation
  Unsharp filter

## Slide 8: How to find edge image?
We ultimately want image of a binary mask of where there is an edge.
How to do so?

## Slide 9: First order derivative
Derivative of an edge:
Finding maximum points in the derivative of an image is a possible way to find edges!

## Slide 10: Deriving the derivative
Definition of derivative in continues functions:
In discrete space we can set
And in 2D space (derivative along x axis):
Notes: f’(x)=\lim_{h\to 0}\frac{f(x+h)-f(x)}{h}
f’[x]=f[x+1]-f[x]
f'_{x}[x,y]=f[x+1,y]-f[x,y]

## Slide 11: 1st derivative filter
We can mimic this derivative as a convolution operator:
  Note 1: when a kernel size is even in some dimension, the center of the kernel needs to be specified (above the center is ).
  Note 2: remember that in the convolution operation the kernel is flipped in both directions.
Notes: f_x'=
f*\begin{array}{|c|c|}
\hline
+1 & -1 \\
\hline
\end{array}

## Slide 12: Symmetric 1st derivative
A more common approach is using the symmetric 1st derivative:
Which translates to this kernel:
We’ll use the kernel above without the constant, since we only care about the ratio between gradients.
Notes: f'(x)=\lim_{h\to 0}\frac{f(x+h)-f(x-h)}{2h}
f_x'=
f*\frac{1}{2}\begin{array}{|c|c|c|}
\hline
+1 & \; 0 \; & -1 \\
\hline
\end{array}

## Slide 13: Y direction
The convolution kernel above is true for python/matlab/opencv image axis convention, where the positive y direction is down.

## Slide 14: Image gradient
The gradient of an image:
The gradient points in the direction of most rapid increase in intensity:
The edge strength is given by the gradient magnitude:

## Slide 15: Gradient direction
The gradient direction is given by:
is determined by the right-hand rule from axis.
Notes: \theta = atan2(-f'_y,f'_x)
\operatorname{atan2}(y,x) =
\begin{cases}
\arctan(\frac y x) &\text{if } x > 0, \\
\arctan(\frac y x) + \pi &\text{if } x < 0 \text{ and } y \ge 0, \\
\arctan(\frac y x) - \pi &\text{if } x < 0 \text{ and } y < 0, \\
+\frac{\pi}{2} &\text{if } x = 0 \text{ and } y > 0, \\
-\frac{\pi}{2} &\text{if } x = 0 \text{ and } y < 0, \\
\text{undefined} &\text{if } x = 0 \text{ and } y = 0.
\end{cases}

## Slide 16: Image gradient example

## Slide 17: Prewitt filter
The same as before but more robust to noise since it uses the diagonal neighbors as well.
Notes: f_x'=
f*\begin{array}{|c|c|c|}
\hline
+1 & \; 0 \; & -1 \\
\hline
+1 & \; 0 \; & -1 \\
\hline
+1 & \; 0 \; & -1 \\
\hline
\end{array}

## Slide 18: Noise effects
Hard to find maximum of derivative in noisy environment.
Noisy input image

## Slide 19: Solution: smoothing the noise
Search for the maximum in the smooth image!
f
h
f * h

## Slide 20: Gaussian derivative kernel
Using this convolution trick:
derivative of Gaussian
output (same as before)
input
Notes: \frac{d}{dx}(h*f)=(\frac{d}{dx}h)*f

## Slide 21: Gaussian derivative kernel 2D
x-direction
y-direction
Derivative of Gaussian

## Slide 22: Sobel filter
Common approximation of derivative of Gaussian
Can also be thought of as Prewitt with higher weighting for closer neighbors.
In theory- should give better performance relative to Prewitt since it includes smoothing effect.
In practice- non definitive superiority to Prewitt (3X3 kernel is a rough approximation…).
1 | 0 | -1
2 | 0 | -2
1 | 0 | -1
1 | 2 | 1
0 | 0 | 0
-1 | -2 | -1

## Slide 23: Table of content
Intro to edges
Basic edge image
Edge thinning
  LoG
  NMS
Edge mask
Canny edge detector
Other edge related topics
  Frequency representation
  Unsharp filter

## Slide 24: Edge thinning
I have the edge filter result, but I want only one pixel to represent the edge in a binary mask.
How do I find this?

## Slide 25: Naïve approach: 2nd derivative
Let’s try to find the zero crossing of the 2nd derivative.
Only single zero crossing- should produce thinner edge

## Slide 26: LoG
Lets take the 2nd derivative of the Gaussian (Laplacian of Gaussian: LoG) kernel so smoothing will help with noise reduction:
Laplacian of Gaussian
Notes: \Delta f = \nabla^2 f = \nabla \cdot \nabla f = \nabla \cdot [\frac{df}{dx},\frac{df}{dy}]=\frac{d^2f}{dx^2}+\frac{d^2f}{dy^2}

## Slide 27: Find edge in noise signal: LoG
Input is noisy step signal, output is zero crossing at the step.
Laplacian of Gaussian
output
input

## Slide 28: LoG quantization
Can be filter of different sizes:
  3X3:
  9X9:
0 | 1 | 0
1 | -4 | 1
0 | 1 | 0
1 | 1 | 1
1 | -8 | 1
1 | 1 | 1

## Slide 29: DoG
Can also use difference of Gaussians (DoG) to mimic LoG.
Why do we want to do this? Because we can…

## Slide 31: Example: LoG
Laplacian of Gaussian filtering
Derivative of Gaussian filtering

## Slide 32: Example: LoG
Note: both images are after absolute value.
Laplacian of Gaussian filtering
Derivative of Gaussian filtering
zero-crossing
peak

## Slide 33: Zero crossing
The new problem arising from the LoG filter is: how to mark the zero crossings?
Answer: no easy algorithm to detect zero crossings.
  E.g.: planes with minor noise will also produce zero crossing artifacts.

## Slide 34: Table of content
Intro to edges
Basic edge image
Edge thinning
  LoG
  NMS
Edge mask
Canny edge detector
Other edge related topics
  Frequency representation
  Unsharp filter

## Slide 35: Edge thinning
I have the edge filter result, but I want only one pixel to represent the edge in a binary mask.
How do I find this?

## Slide 36: Non maximum suppression
NMS
Find the gradient magnitude + orientation of each pixel and search on this 1D line for maximum point.

## Slide 37: NMS algorithm
get image gradient magnitude + orientation using 1D 3X3 gradient filter (e.g.: Sobel).
for each pixel :
  Quantize to one of four possibilities: .
  In 3X3 neighborhood of , find two neighbors in quantized gradient orientation .
  If

## Slide 38: NMS results
Before NMS
After NMS

## Slide 39: Table of content
Intro to edges
Basic edge image
Edge thinning
  LoG
  NMS
Edge mask
Canny edge detector
Other edge related topics
  Frequency representation
  Unsharp filter

## Slide 40: Edge mask
How do we transform this integer image to a binary mask of where there is/ isn’t an edge?

## Slide 41: First try: single threshold edge mask
Mask == binary image.
Possible 1st solution- thresholding:
  Choose an TH edge value, above which the pixel mask is 1, 0 otherwise.
  The value can be a constant or percentile of the maximum edge value exists in the image.
  Low TH: will get extra edges, but also input noise.
  High TH: can miss lower valued edge pixels, less noise.
How can we difference between low value edge pixels and noise?

## Slide 42: Hysteresis motivation
Weak edges are usually neighbors of strong edges, while noise can be at any pixel.
  Usually “neighbors” means 3X3 square of adjacent pixels.
If we know that a neighbor of a weak edge is a strong edge, then the weak edge is a strong edge!

## Slide 43: hysteresis
Choose two thresholds:
For each pixel :
  If
  elif
  Else: //
  While that are neighbors of exists:
    for each:
    If neighbor of :
  All remaining
Schmitt trigger hysteresis example plot

## Slide 44: Table of content
Intro to edges
Basic edge image
Edge thinning
  LoG
  NMS
Edge mask
Canny edge detector
Other edge related topics
  Frequency representation
  Unsharp filter

## Slide 45: Canny edge detector
Canny edge detector is one of the most known and used CV algorithms, still highly used even today (developed in 1986):
  Gaussian filter
  Find image gradient magnitude and orientation
  NMS
  Hysteresis

## Slide 46: Example output

## Slide 47: Different Gaussians
Stronger smoothing will cause only “large-scale” gradients to remain (more on scaling- later in class).
Canny with
Canny with
original

## Slide 48: Important note: tradeoffs
It’s a common misconception in CV to think that one algorithm is always better than another.
In CV, algorithms are highly dependent in the given environment in which they are executed. Each environment can vary in:
  Noise.
  Needed computation efficiency.
  Overall problem variance.
  Etc…
CV is the land Of
tradeoffs

## Slide 49: Table of content
Intro to edges
Basic edge image
Edge thinning
  LoG
  NMS
Edge mask
Canny edge detector
Other edge related topics
  Frequency representation
  Unsharp filter

## Slide 50: HP filter
Higher frequencies represents the edges of images.
Removing the lower frequencies of an image will result in edge image!

## Slide 51: Different edge filters

## Slide 52: Why prewitt has waves?
Recalling the mean filter – we can say that prewitt is like two side by side rectangles.
Sobel is like two gaussians side by side!

## Slide 53: Table of content
Intro to edges
Basic edge image
Edge thinning
  LoG
  NMS
Edge mask
Canny edge detector
Other edge related topics
  Frequency representation
  Unsharp filter

## Slide 54: Image sharpening
Obtain the high frequencies magnitude image.
Enhance the edges (e.g. by multiplying with a constant>1).
Add the enhanced edges back to the original image.
One liner:
Notes: f_{sharpen} = f + \gamma \cdot ||\triangledown f||

## Slide 55: Unsharp filter
The former can also be done with only low pass filtering!
This was also the way that photographers enhanced edges before CV (dates to the 1930s). More on this topic here: https://en.wikipedia.org/wiki/Unsharp_masking#Photographic_darkroom_unsharp_masking
Notes: f_{unsharp} = f + \gamma (f- h_{blur}*f)